## Slide 1
Graph Theory, Topological Analysis
ECE 580
12
Graph Theory, Topological Analysis - Terms
Topological Analysis: General, systematic, suited for CAD
Graph: Nodes and directed branches, describes the topology of the circuit, ref. direction. Helps visualize CAD
Tree: Connected subgraph containing all nodes but no loops
Branches in tree: Twigs
Branches not in the tree: Links
Links: Cotree
Notes: 1
1

## Slide 2
Graph Theory, Topological Analysis
ECE 580
12-b
Graph Theory, Topological Analysis
Analysis steps:
KCL
KVL
Branch Relations
Linear equations: N3 operations
Sparse ~ N
Notes: 2
2

## Slide 3
Graph Theory, Topological Analysis
ECE 580
12-c
Graph Theory, Topological Analysis
Note the very high-resistance Rbougs1 and Rbogus2 resistors in the netlist (not shown in the schematic for brevity) across each input voltage source, to keepSPICE from think V1 and V2 were open-circuited, just like the other op-amp circuit examples.;
Notes: 3
3

## Slide 4
Graph Theory, Topological Analysis
ECE 580
12-d
Graph Theory, Topological Analysis
Note the very high-resistance Rbougs1 and Rbogus2 resistors in the netlist (not shown in the schematic for brevity) across each input voltage source, to keepSPICE from think V1 and V2 were open-circuited, just like the other op-amp circuit examples.;
ECAP
CANCER
SPICE
Notes: 4
4

## Slide 5
Graph Theory, Topological Analysis
ECE 580
13-a
Graph Theory, Topological Analysis
Incidence Matrix A: Describes connectivity between nodes and branches
Rules for aij
  +1, if branch j is directed away from node i
  - 1, if branch j is directed toward node i
  0, if branch j is not incident with node i
As an example, the node-to-branch incidence matrix for the graph of Fig. 2.2b
Augmented incidence matrix: Contains reference node (0)
Notes: 5
5

## Slide 6
Graph Theory, Topological Analysis
ECE 580
13-b
Graph Theory, Topological Analysis
Row: Nodes; Column: Branches
One row may be omitted, since sum of entries in each column is zero. (Reference node omitted)
Resulting matrix: A. # of non-reference nodes N < # of branches B  Rank of A < N
Partitioned incidence matrix: Choose a tree, put its twigs in the first N columns of A. Then:
A = [ A t | A c ] ; Nonsingular A t  det { A t } != 0
It can be shown that det { A t } = + 1; and that det { A At } = # of trees.
This proves rank A = N! Largest nonsingular submatrix is N x N.
Notes: 6
6

## Slide 7
Graph Theory, Topological Analysis
ECE 580
13-c
Graph Theory, Topological Analysis
Notes: 7
7

## Slide 8
Graph Theory, Topological Analysis
ECE 580
14
Graph Theory, Topological Analysis
Graph Definitions
These trees can be found by systematically listing possible combinations of the three branches. These are listed below.
Each entry in the list must now scrutinized to see if it contains all nodes and no loops
Notes: 8
8

## Slide 9
Graph Theory, Topological Analysis
ECE 580
15-a
Graph Theory, Topological Analysis
Branch-to-Node Voltage Transformation: (KVL)
Branch Voltage Vector: Vt =[v1,v2,…,vB]
Node Voltage Vector: Et = [e1,e2,…,eN]
By KVL, if branch k goes from node i to node j, so aik = 1 and ajk = -1, then
Vk = ei – ej = aikei + ajkej = [kth column of A]t E = aikei+…+aNkeN
In general V = AtE Vk = ei - ej
Branch voltages expressed in terms of node voltages  there are fewer
Purpose: formulate smallest set of linear equations before solving them
Notes: 9
9

## Slide 10
Graph Theory, Topological Analysis
ECE 580
15-b
Graph Theory, Topological Analysis
KCL in Topological Formulation
KCL says the sum of currents leaving any node is zero.
Since aij= 1(-1) means branch j leaves (enters) node i, KCL for node i means:
  Where I = [i1,i2,…,iB] and 0 = [0,0,….0]
Choose a tree, and partition A and I so that A = {At|Ac} & It = {It|Ic}
Then AtIt + AcIc = 0 and It= -(At)-1AcIc.
This gives the twig currents from A and the link currents. Note At cannot be singular
Notes: 10
10

## Slide 11
Graph Theory, Topological Analysis
ECE 580
16
Graph Theory, Topological Analysis
Example
Twig currents can be found from link current. Fewer twigs than links.
Notes: 11
11

## Slide 12
Generalized Branch Relations
ECE 580
17-a
Generalized Branch Relations
Generalized Branch Relations; S-domain!
General branch for lumped linear network contains a (single) element bk which may be an R,L,C and dependent sources as well as a voltage and current source which may include the representation of initial energy stored in bk
Since ik’=ik-Jk and vk’= vk – VkE
For the branch vectors I’ = I – J & V’= V – VE hold
Notes: 12
12

## Slide 13
Generalized Branch Relations
ECE 580
17-b
Generalized Branch Relations
Nodal Analysis
Combining the branch relations with the KVL (V’= ATE) and KCL (AI’=0) gives the matrix relations
            V = VE + ATE
            AI = AJ
Result 2 equations , 3 unknown vectors
            3. I = YV
Let the V-I relations of the bk elements by described by the matrix relation I = YV, where the diagonal element yii of Y represents the internal admittance of the bi in branch I, and the off-diagonal one ykl = ik/vl represents a dependent I source of branch k controlled by Vl. By combining (1),(2) and (3), and eliminating V and I in the Laplace domain, the nodal equations YN(s)E(s) = JN(s) result, where YN(s) = AY(s)At is the N x N nodal admittance matrix, and JN(s) = A[J(s)-Y(s)VE(s)] the equivalent nodal current excitation vector. (Due to independent sources Jk and Vke)
Notes: 13
13

## Slide 14
Generalized Branch Relations
ECE 580
18
Generalized Branch Relations
Node analysis Parameters:
Notes: 14
14

## Slide 15
Generalized Branch Relations
ECE 580
19
Generalized Branch Relations
Example
I9 = G9V9 + gmV6
Notes: 15
15

## Slide 16
Generalized Branch Relations
ECE 580
20
Generalized Branch Relations
Notes: 16
16

## Slide 17
Generalized Branch Relations
ECE 580
21-a
Generalized Branch Relations
Notes: 17
17

## Slide 18
Generalized Branch Relations
ECE 580
21-b
Generalized Branch Relations
Notes: 18
18

## Slide 19
ECE 580
30
Node Analysis Summary
A | Incidence Matrix, all analysis in s domain
Kirchhoff’s Laws: | 
V = AtE | V: branch Voltage Vector E: node Voltage Vector
AI = 0 | I: branch Voltage Vector 0: zero Vector
Branch Relations: | 
I’ = I - J | I’: branch current vector I: element current vector J: source current vector
V’= V –VE | V’: branch voltage vector V: element voltage vector VE: source voltage vector
I = YV | Y: branch admittance matrix
Combining Relations: | 
YN = AYAt | YN: node admittance matrix
V’= V –VE | JN: node current excitation matrix
YNE = JN | Generalized node equations
Notes: 19
19