## Slide 1: Quasi-Passive Cyclic DAC
Gabor C. Temes
School of EECS
Oregon State University

## Slide 2: Outline
Quasi-Passive Cyclic DAC
  Operation
Capacitor Mismatch and Mismatch Compensation
  Capacitor mismatch
  Mismatch compensating switching
  Spectrum shaping
  Radix-based digital correction
Two-Capacitor DAC Enhancements
  Time interleaved 2-C DACs
  Pipelined quasi-passive cyclic DAC

## Slide 3: Quasi-Passive Cyclic DAC
Operation:
  Charge redistribution between two equal-valued capacitors
  Serial digital input; LSB first
  Φ1 and Φ2 are two non-overlapping clock phases
  Conversion follows equation
DAC basic architecture
Conversion sequence for input ‘1101’
[1] R. E. Suarez et al., “All-MOS charge distribution analog-to-digital conversion techniques – Part II,” JSSC, Dec. 1975, pp. 379-385.
Notes: Topright circuit shows the basic structure of 2-C DAC
Waveforms illustrate change of voltages across capacitors C1 and C2

## Slide 4: Capacitor Mismatch
Capacitor mismatch effects
  Conversion accuracy limited by capacitor matching
  Capacitor mismatch introduces nonlinearity
  Plots show performance degradation (bottom) in SNDR and SFDR compared with output spectrum from DAC with ideal matching (top)
Notes: 214 point FFT

## Slide 5: Mismatch Compensation (1)
Switching techniques
  Compensative switching
    The roles of the two capacitor is interchangeable
    The roles of the capacitors can be chosen on bit-wise base
    An algorithm was developed to minimize the conversion error for any digital word
    The switching pattern is input dependent
    First-order error canceled for 31% of the input codes; reduced to 1/10 for 48% of the input codes
[2] Weyten, L.; Audenaert, S., "Two-capacitor DAC with compensative switching," Electronics Letters , vol.31, no.17, pp.1435-1437, 17 Aug 1995.
The roles of the two capacitors are interchangeable with additional switches
Notes: Note that not all input codes can be compensated.
Need only N cycles to convert

## Slide 6: Mismatch Compensation (2)
Switching techniques
  Complementary switching
    Digital word fed to 2-C DAC twice; once with normal arrangement, once with swapped roles of C1 and C2
    Output sof the two conversions are added (or averaged)
    First-order mismatch compensated at cost of doubled conversion time
[3] Rombouts, P.; Weyten, L., "Linearity improvement for the switched-capacitor DAC," Electronics Letters , vol.32, no.4, pp.293-294, 15 Feb 1996.
Notes: Need 2N cycles
Cancel only 1st order error, higher order error can be prominent when resolution is high

## Slide 7: Mismatch Compensation (3)
Switching techniques
  Input-word-splitting compensative switching
    Compensative switching [2] does not compensate for all input codes
    Split digital input into sum of two digital codes
    The conversion errors need to be able to be respectively compensated using compensative switching for the two new digital inputs
    Final output is the sum of the two conversions
    Needs two sets of 2-C DACs
    Needs analog summation
    Needs sophisticated algorithm for splitting the input word
[4] Rombouts, P.; Weyten, L.; Raman, J.; Audenaert, S., "Capacitor mismatch compensation for the quasi-passive-switched-capacitor DAC," Circuits and Systems I: Fundamental Theory and Applications, IEEE Transactions on , vol.45, no.1, pp.68-71, Jan 1998.

## Slide 8: Mismatch Compensation (4)
Switching techniques
  Alternately complementary switching
    Roles of C1 and C2 are swapped alternately in the first cycle and adopt complementary switching [3] for the second conversion cycle
    Output of the two conversions are summed (or averaged)
    INL improved due to cancellation of major second-order error
  Hybrid switching
    Averaging conversion results of complementary switching and alternately complementary switching
    Smaller INL; fourfold conversion cycles
[5] Poki Chen; Ting-Chun Liu, "Switching Schemes for Reducing Capacitor Mismatch Sensitivity of Quasi-Passive Cyclic DAC," Circuits and Systems II: Express Briefs, IEEE Transactions on , vol.56, no.1, pp.26-30, Jan. 2009
Notes: Paper shows a 3-fold average INL improvement for hybrid switching compared with complementary switching

## Slide 9: Mismatch Compensation (5)
Mismatch shaping
  Using oversampling ΔΣ Modulator
    Digital state machine to control switching sequence of a symmetric two-capacitor DAC
    Improved linearity; better shaping for higher OSR
    Needs 2N clock cycles for N-bit D/A
[6] Steensgaard, J.; Moon, U.-K.; Temes, G.C., "Mismatch-shaping serial digital-to-analog converter," Circuits and Systems, 1999. ISCAS '99. Proceedings of the 1999 IEEE International Symposium on , vol.2, no., pp.5-8 vol.2, Jul 1999
Simulated (FFT) performance of the DAC without (a) and with (b) mismatch shaping using a second-order loop filter

## Slide 10: Mismatch Compensation (6)
Radix-Based Digital Correction
  Compensation in digital domain
    Effectively a radix-(C1/C2) conversion
    Assumes known mismatch 2(C1-C2)/(C1+C2), or C1/C2
    ADC-like algorithm predistorts digital input
    Feeds predistorted digital words into the 2-C DAC
    Better performance when DAC resolution is high
    Need to find mismatch with high accuracy
DAC output spectra plots for (a) uncompensated condition, (b) alternately complementary switching, (c) radix-based algorithm and (d) radix-based algorithm with one extra bit.
Radix-based digital pre-distortion algorithm flowchart
Notes: Need to arrange C1 and C2 in such a way that C2, or the redistribution capacitor need to be the larger one. (conversion radix < 2)

## Slide 11: Two-Capacitor DAC Variations
Time interleaved 2-C DAC
  Time interleaving 2-C blocks improves throughput speed
  Capacitor mismatch among channels tolerable
  Direct-charge-transfer buffer reduces power consumption
Pipelined quasi-passive cyclic DAC
  Same operation as 2-C DAC
  Information passed on to the last capacitor and DCT output buffer
[7] Wang, F.-J.; Temes, G.C.; Law, S., "A quasi-passive CMOS pipeline D/A converter," Solid-State Circuits, IEEE Journal of , vol.24, no.6, pp.1752-1755, Dec 1989
Notes: More about the pipelined structure presented separately