CITY OF ALBANY, OREGON

## GEOGRAPHIC INFORMATION SERVICES

# DIGITAL PLANIMETRIC MAPPING STANDARDS

FEBRUARY 1998

J:\airmaps\layerlst.wri

ARC/INFO		LAYER #	LAYER		LAYER		 				LAYER			DEFAULT

COVERAGE NAME	RANGE	NAME (#)	DESCRIPTION					COLOR		STATUS

A_SURVEY		000-079	001		Vertical Control					241		 	On

002		Vertical Control Text				241		 	On

003		Horizontal/Vertical GPS Control			241			On

004		Horizontal/Vertical GPS Control Text		241			On

010		Grid Lines					White			On

011		Grid Symbols					White			On

012		Grid Text					White			On

020		Section Corner					241			On

021		Section Corner Text				241			On

030		DLC Corner					241			On

031		DLC Corner Text				241			On

CNTYLINE		080-099	080		County Line					87			On

081		County Line Text				87			On

TRNSPORT		100-199	100		Paved Road Edge				White			On

101		Paved Road Centerline				Red			Frozen

102		Paved Road Text				White			On

105		Unpaved (Gravel) Road Edge			White			On

106		Unpaved Road Centerline			Red			Frozen

107		Unpaved Road Text				White			On

110		Unimproved (Dirt) Road Edge			8			On

111		Unimproved Road Centerline			Red			Frozen

112		Unimproved Road Text				White			On

TRNSPORT (con't.)			115		Road Under Construction Edge			8			On

116		Road Under Const. Centerline			Red			Frozen

117		Road Under Const. Text				White			On

120		Interstate Highway Edge			White			Not Used

121		Interstate Highway Centerline			Red			Not Used

122		Interstate Highway Text				White			Not Used

125		State Highway Edge				White			Not Used

126		State Highway Centerline			Red			Not Used

127		State Highway Text				White			Not Used

130		Traffic Signal					Red			On

131		Traffic Sign					Red			On

140		Curb Line					234			On

141		Shoulder					8			On

142		Block Closure Line				White			Frozen

143		Fog Line					White			On

150		Overpass					White			On

151		Ramp						White			On

152		Tunnel						White			On

153		Guard Rail					245			On

154		Bridge						245			On

155		Under Bridge Information			8			Frozen

160		Driveway - Surfaced				White			On

161		Driveway - Unsurfaced				8			On

162		Driveway - Curbing				234			On

163		Parking Lot - Paved				White			On

164		Parking Lot - Paved Text			White			On

165		Parking Lot - Unpaved				8			On

166		Parking Lot - Unpaved Text			White			On

167		Parking Lot - Curbing				234			On

168		Parking Lot Barrier Curbs (Wheelstops)		234			On

169		Sidewalk - Concrete (Public)			White			On

170		Sidewalk - Paved (Public)			8			On

171		Sidewalk Segments in Driveways		White			Frozen

172		Trail						8			On

TRNSPORT (con't.)			180		Railroad - Active				55			On

181		Railroad - Inactive				53			On

182		Abandoned RR Grade				53			On

183		RR Xing Symbol				55			On

184		RR Switch Symbol				55			On

185		Hidden RR Information				8			On

186		RR Text					55			On

190		Airport Runway					White			On

191		Airport Runway Centerline			Red			Frozen

192		Airport Taxiway					White			On

193		Airport Lighting					Yellow			On

194		Airport Paint Lines				8			On

195		Airport Hangars					204			On

196		Helicopter Pad					White			On

197		Airport Text					White			On

BUILDING		 200-299	200		Building						204			On

201		Building Under Construction			204			On

202		Obscured Building Line				204			On

203		Building Ruins					8			On

204		Building Text					204			On

205		Disturbed Ground				200			On

206		Disturbed Ground Text				200			On

STRCTURE		 300-399	300		Overhead Walk					44			On

301		Deck						44			On

302		Private Walkways				White			On

303		Platform					44			On

304		Loading Dock					White			On

305		Swimming Pool					Blue			On

306		Transit Shelter					White			On

307		Greenhouse					White			On

308		Fuel Tank					White			On

309		Silo						White			On

310		Hopper						White			On

311		Windmill					White			On

312		Fence						45			On

313		Gate						45			On

314		Retaining Wall					White			On

315		Non-Retaining Wall				White			On

STRCTURE (con't.)			316		Stone Wall					White			On

317		Pipeline						White			On

318		Billboard					Red			On

319		Large Sign - Commercial			Red			On

320		Small Sign					Red			On

321		Post						White			On

322		Flagpost					White			On

323		Satellite Dish					White			On

324		Monument					White			On

325		Planter Box					White			On

326		Cemetery					White			On

327		Cemetery Text					White			On

328		Gas Pump					White			On

329		Steps/Stairs					White			On

330		Telephone Booth				White			On

331		Concrete Line					White			On

332		Concrete Line Text				White			On

350		Golf Course Tee				81			On

351		Golf Course Greens				81			On

352		Golf Course Sandtraps				41			On

353		Golf Course Fairways				81			On

354		Paved Golf Path				8			On

355		Golf Course Text				White			On

360		Track						White			On

361		Sport Field					8			On

362		Bleachers					White			On

363		Basketball Court				White			On

364		Tennis Court					White			On

365		Playground					White			On

366		Horseshoe Pit					White			On

367		Paved Bike Path				8			On

368		Recreation Text					White			On

370		General Misc. Structure				White			On

380		Rip-Rap					White			On

381		Rock/Rock Outcrop				White			On

STRCTURE (con't.)			390		Boom						White			On

391		Boat Ramp					White			On

392		Dock						White			On

393		Buoy						White			On

394		Pylon/Piling/Dolphin				White			On

ELECTRIC		 400-499	400		Light Pole					Yellow			On

401		Light - Symbol					Yellow			On

402		Light - Standard					Yellow			On

403		Light - Double Standard				Yellow			On

404		Luminaire					Yellow			On

410		Power Pole					30			On

411		Power Line					30			On

412		Power Manhole					30			On

413		Power Manhole Text				30			On

414		Transmission Line Tower			30			On

415		Transmission Line				30			On

416		Guy Wire					30			On

417		Utility Box/Vault					30			On

418		Power Substation				30			On

420		Radio Tower					White			On

421		Posts- Electrical					31			On

430		Un -I.D. Utility Line				221			On

431		Un-I.D. Manhole				11			On

432		Un-I.D. Manhole Text				11			On

WATER	 	450-499	450		Water Line					Cyan			[FUTURE]

451		Water Tank					Cyan			On

452		Water Reservoir				Cyan			On

453		Water Valve					Cyan			On

454		Water Valve Text				Cyan			On

455		Fire Hydrant					Cyan			On

456		Fire Hydrant Text				Cyan			On

457		Water Meter					Cyan			On

460		Water Treatment Plant				204			On

461		Water Treatment Plant Lagoon			Blue			On

UTILITY		500-599	500		Sanitary Sewer Line				Green			[FUTURE]

501		Sanitary Sewer Manhole			Green			On

502		Sanitary Sewer Manhole Text			Green			On

503		Non-City Manhole				122			On

504		Non-City Manhole Text				122			On

505		Sewer Lift Station				Green			On

506		Cleanout					Green			On

510		Sanitary Sewer Treatment Plant			204			On

515		Gas Valve					51			On

516		Gas Valve Text					51			On

550		Storm Drain Line				Magenta		[FUTURE]

551		Storm Drain Manhole				Magenta		On

552		Storm Drain Manhole Text			Magenta		On

553		Catch Basin					Magenta		On

554		Catch Basin Text				Magenta		On

555		Curb Inlet					Magenta		On

556		Curb Inlet Text					Magenta		On

557		Culvert - Outline				Magenta		On

558		Culvert - Symbol				Magenta		On

560		Overflow Intake					White			On

570		Storm Drainage Outfall				Magenta		On

571		Detention Pond					Blue			On

580		Private Catch Basin 				8			On

581		Private Catch Basin Text			8			On

582		Private Storm Drain Manhole			8			On

583		Private Storm Drain Manhole Text		8			On

TOPO			600-649	600		Break Line					Red			Frozen

601		DTM Spot					Red			Frozen

602		DEM Grid					Red			Frozen

603		Road Centerline Points				(Arc/Info Conversion Only)

CONTOUR		650-699	650		Index Contour					250			On

651		Obscured Index Contour			250			On

652		Depression Index Contour			250			On

653		Obscured Depression Index Contour		250			On

654		Hidden Index Contour				250			On

655		Hidden Index Label Segment			250			Frozen

656		Index Label Text				250			On

657		Intermediate Contour				251			On

658		Obscured Intermediate Contour			251			On

659		Depression Intermediate Contour		251			On

660		Obscured Depression Intermediate Contour	251			On

661		Hidden Intermediate Contour			251			On

662		Hidden Intermediate Label Segment		251			Frozen

663		Intermediate Label Text				251			On

670		Spot Elevation Symbol				8			On

671		Spot Elevation Text				8			On

VEGETATE		700-749	700		General Tree Line				60			On

701		General Tree Line Text				60			On

702		General Brush Line				60			On

703		General Brush Line Text			60			On

704		Ground Not Visible Line				Red			Frozen

705		Large Deciduous Tree				60			On

706		Large Evergreen Tree				60			On

707		Shrub						60			On

708		Orchard Line					60			On

709		Orchard Text					60			On

710		Hedge						60			On

750		Lowland - Outline				Green			On

751		Lowland - Symbol				Green			On

MISCLAND		800-849	800		Landfill						White			On

801		Dump						White			On

802		Quarry/Mine					White			On

803		Gravel Pit					White			On

804		Borrow Pit					White			On

805		Stockpile					White			On

806		Excavation Feature Text			White			On

A_HYDRO		850-899	850		River						Blue			On

851		River Name Text				Blue			On

860		Perennial Stream				Blue			On

861		Approximate Stream				150			On

862		Stream Name Text				Blue			On

870		Canal						Blue			On

871		Canal Name Text				Blue			On

880		Shoreline (Lake, Pond, etc.)			Blue			On

881		Lake, Pond, etc, Name Text			Blue			On

890		Ditch Centerline					Blue			On

891		Rapids						Blue			On

892		Falls						Blue			On

893		Well						Blue			On

894		Spring						Blue			On

895		Gaging Station					White			On

896		Dam (Man Made)				White			On

897		Flow Arrow					Blue			On

898		Flume						White			On

899		Spillway					White			On

TITLE			900-904	900		Large Title Block Text				White			On

901		Medium Title Block Text				White			On

902		Small Title Block Text				White			On

903		Misc. Text/Notes				White			On

904		Areas of Change (Polygons)			Red			Frozen

LOGO			905-919	905		City Logo					White			On

906		Sheet Index					White			On

910		Symbol Legend					White

LEGEND		920-925	920		Border Line					White			On

921		Trim Line					White			On

922		Match Line					White			On

923		Match Line Text					White			On