# Instructions for Using the Utility Network Analyst Toolbar with NHD Data in ArcMap

# Using The ArcMap Utility Network Analyst Toolbar With NHD Data Downloaded From Gateway:

To model up/down stream flow using the Utility Network Analyst toolbar in ArcMap, you must order the ESRI File GeoDatabase Format. The network will be pre-built by as a layer by Gateway if there are less than 100,000 features.

## Navigating NHD Flow Path – adapted from http://nhd.usgs.gov/NHD_QuickStart_Sept_05.pdf

NHD's flow network allows for analysis to find all paths upstream or downstream of a given point. This is important for water quality modeling; for example, to understand problems such as the spread of invasive species throughout a river system, point source pollution, etc. It is possible to navigate the NHD Flow Path upstream or downstream from any point on the NHDFlowline network using the Utility Network Analyst, a standard Toolbar in ArcMap. You can view navigation results (under Analysis (Options…Results) as a drawing in your ArcMap display window or as a selection.

- Open ArcMap and click on Customize, Toolbars, and check the "Utility Network Analyst" box.

Using Barton County, MO as an example…

- Bring the “nhd24ksn_l_mo011” layer into your ArcMap session.

- “nhd24ksn_l_ mo011” will appear automatically in the Network box within the Utility Network Analyst toolbar.    “nhd24ksn_l_... mo011” references the “nhd24ksn_l_mo011_Junctions” layer.

- Click on the Add Edge Flag Tool . The flag marks the start of the navigation path. You can also see there is an option for a Junction Flag Tool . This flag must be placed on a junction. The other two options allow for the addition of a barricade along the flow path. There is a Junction Barrier Tool , and an Edge Barrier Tool .

- Change the Trace task to Trace Downstream or Trace Upstream. Trace Upstream- finds all paths upstream including tributaries and branches. Trace Downstream- finds all paths downstream including divergences.

- Click the Cursor at the appropriate point on any NHDFlowline to set your starting navigation location. The entire NHDFlowline feature will be included in the navigation result.

- Click on the Solve icon  located at the right end of the Utility Network Toolbar. The navigation will highlight the appropriate NHD Flowlines .

The beginning point is the green flag. The red line shows the upstream trace.	Note: Click Flow (Display Arrows to show 									flow direction.

Click here for more information on the Utility Network Analyst Toolbar, from the ESRI Help pages.